Linux Display Subsystem

---
X Server and Wayland Compositor
https://upload.wikimedia.org/wikipedia/commons/2/2d/The_Linux_Graphics_Stack_and_glamor.svg

---
Wayland Display Server and EGL
https://www.wikiwand.com/ja/Wayland

---
Direct Rendering Manager (DRM)
Direct Rendering Manager
Management of buffers and free space within that memory.
Solve Frame buffer driver cannot be used GPU and multi-user process.
DRM consists of
KMS : Kernel Mode Setting
Change resolution and depth
DRI : Direct Rendering Infrastructure
Interfaces to access hardware directly
GEM : Graphics Execution Manager
Buffer management
DRM Driver in kernel side
Access hardware

---
Direct Rendering Manager (DRM)
If no use DRM

---
Direct Rendering Manager (DRM)
Use DRM

---
Kernel Mode Setting (KMS)
- KMS device model
  - CRTCs
  - Connectors
  - Encoders
  - Planes
- Kernel Mode Setting
  - screen resolution
  - color depth and
  - refresh rate

---
Kernel Mode Setting (KMS)
https://www.kernel.org/doc/html/v4.15/gpu/drm-kms.html

---
Kernel Mode Setting (KMS)
https://www.kernel.org/doc/html/v4.15/gpu/drm-kms.html

---
Video Frame Buffer
The frame buffer device provides an abstraction for
the graphics hardware.
Application
memory
User Space
MMAP
Kernel Space
memory
FB Driver

---
Kernel Mode Setting (KMS)
Encode
Connecter
CRTC
FrameBuffer
Planes

---
LCD Parameters
- VBPD : vertical back porch
- VFBD : vertical front porch
- VSPW : vertical sync pulse width
- HBPD : horizontal back porch
- HFPD : horizontal front porth
- HSPW : horizontal sync pulse width

---
LCD Display Parameters
- Dotclock
  - The video hardware draws pixels on the display speed
dotclock = (X-resolution + left margin +
        right Margin + HSYNC length) *
        (Y-resolution + upper margin +
        lower margin + VSYNC length) * refresh rate
pixclock = 1/dotclock

---
LCD Display Parameters

---
LCD Display Parameters

---
LCD Display Parameters

---
 LCD Display Parameter

---
 LCD Display Parameter