### [1] LED Control From SysFS
1. Control LED
[Target Board ] / [CMD] cd /sys/class/leds / [CMD] cd user-led2/ / [CMD] cat trigger / none rc-feedback kbd-scrolllock kbd-numlock kbd-capslock kbd-kanalock kbd-shiftlock kbd-altgrlock kbd-ctrllock kbd-altlock kbd-shiftllock kbd-shiftrlock kbd-ctrlllock kbd-ctrlrlock mmc0 mmc1 timer oneshot [heartbeat] gpio cpu0 cpu1 cpu2 cpu3 cpu4 cpu5 default-on rfkill0 mmc2 rfkill1 rfkill2 / # change trigger type shot [ This is just a sample, please try to change another type ] / [CMD] echo oneshot > trigger / [CMD] cat trigger / none rc-feedback kbd-scrolllock kbd-numlock kbd-capslock kbd-kanalock kbd-shiftlock kbd-altgrlock kbd-ctrllock kbd-altlock kbd-shiftllock kbd-shiftrlock kbd-ctrlllock kbd-ctrlrlock mmc0 mmc1 timer [oneshot] heartbeat gpio cpu0 cpu1 cpu2 cpu3 cpu4 cpu5 default-on rfkill0 mmc2 rfkill1 rfkill2 / [CMD] echo 1 > shot / # Please check the Blue LED

### [2] GPIO Control From SysFS
1. Control GPIO
[CMD] cd /sys/class/gpio / # To know what attribute in gpiochX [CMD] cat gpiochip0/label / [CMD] cat gpiochip0/base / [CMD] cat gpiochip0/ngpio / # Export GPIO2_B3 [CMD] echo 75 > export / # Check gpio32 attribute [CMD] ls gpio75/ active_low device direction edge power subsystem uevent value / # Please use “cat” cmd to read “all attribution” from gpio32 / [CMD] cat gpio75/direction / # Set GPIO75 is a output function [CMD] echo out > gpio75/direction / # Please check “Read LED” status / # Set GPIO75 is High value / [CMD] echo 1 > gpio75/value # Set gpio75 is Low value [CMD] echo 0 > gpio75/value / # Please change other GPIO about LED and Button # So, please check # 1. schematic (電路圖) NanoPIM4_Extend_V01.pdf, # Rockpi4_v13_sch_20181112.pdf #

### [3] GPIO Control From SysFS with Script
1. Control GPIO
# Use Script to set GPIO from SYSFS / # Below is a Example for controlling GPIO75 / # Below is script content for Sample, please create a led_test.sh file. / # Then put below sample code to led_test.sh / ===================================================================== / #!/bin/bash / GPIO_SYSFS=/sys/class/gpio / CTRL_GPIO=gpio$1 / LED_ONOFF=$2 / echo $GPIO_SYSFS/$CTRL_GPIO / if [ ! -d "$GPIO_SYSFS/$CTRL_GPIO" ]; then / echo $1 > $GPIO_SYSFS/export / echo out > $GPIO_SYSFS/$CTRL_GPIO/direction / fi / if [ $2 = "ON" ];then / echo "LED On" / GPIO_VAL=0 / else / echo "LED Off" / GPIO_VAL=1 / fi / echo $GPIO_VAL > $GPIO_SYSFS/$CTRL_GPIO/value / ===================================================================== / # Test <led_test.sh>, please check LED status / [CMD] sh ./led_test.sh 75 ON / [CMD] sh ./led_test.sh 75 OFF

### [4] Download GPIO Control with C Program
1. Control GPIO with C program
# Download C source code / [CMD] git clone https://github.com/xlloss/embedded_control_app.git / [CMD] cd embedded_control_app/gpio-sysfs-demo [CMD] source ~/set_toolchain.sh / # Check Toolchain is workable $ aarch64-linux-gnu-gcc -v / # Compile the sample gpio-sysfs-demo / [CMD] make / # Put gpioctl gpiodemo to Targetboard [use scp command] / [CMD] scp ./gpioctl ./gpiodemo rock@BOARD_IP:/tmp/ / # Test gpioctl gpiodemo in Target board / [Target Board] / # Test gpioctl / [CMD] /tmp/gpioctl --help / Usage: ./gpioctl [OPTION] ... / Simple gpio access / -h, --help This message / -p, --getin <dio> Returns the input value of n sysfs DIO / -e, --setout <dio> Sets a sysfs DIO output value high / -l, --clrout <dio> Sets a sysfs DIO output value low / -d, --ddrout <dio> Set sysfs DIO to an output / -w, --waitfor <dio> Wait for IO to change to the configured edge / -r, --ddrin <dio> Set sysfs DIO to an input / # Set gpio32 as output function / [CMD] /tmp/gpioctl -d 75 / #Check SysFS about gpio / [CMD] ls /sys/class/gpio / # Please check Red Led status after doing below command. / # Set GPIO75 output is Low / [CMD] /tmp/gpioctl -l 75 / # Set gpio32 output is High / [CMD] /tmp/gpioctl -e 75 / # Test gpiodemo, please try to change control gpoio32 [LED0] from gpiodemo.c / diff --git a/gpio-sysfs-demo/gpiodemo.c b/gpio-sysfs-demo/gpiodemo.c / index f2686ec..3fd7e1f 100644 / --- a/gpio-sysfs-demo/gpiodemo.c / +++ b/gpio-sysfs-demo/gpiodemo.c / @@ -43,7 +43,7 @@ / #define LED_TEST_NUM 1 / /* int led_set[4] = {LED_0, LED_1, LED_2, LED_3}; */ / -int led_set[1] = {LED_G}; / +int led_set[1] = {LED_0}; / pthread_mutex_t mutex; / @@ -182,7 +182,7 @@ int main(int argc, char **argv) { / start_routine[3] = thr_led3; / */ / - start_routine[0] = thr_led_green; / + start_routine[0] = thr_led0; / for (i = 0; i < LED_TEST_NUM; i++) { / led = led_set[i]; / # Re-Compile gpio-sysfs-demo then put gpiodemo to target board / # Please check Red Led status / [CMD] gpiodemo

### [5] SH21 Read From SysFS
(humidity and temperature sensor)
Read Temperature and Humidity
# Modify hw_intfc.conf for enabling i2c7 / [ Target ] / [CMD] vim /boot/hw_intfc.conf / intfc:i2c7=off → intfc:i2c7=on / [CMD] reboot / # Check i2c7 / [CMD] ls /sys/class/i2c-adapter/ -l / # modify DTS (rockpi-4b-linux.dts) / [CMD] vim arch/arm64/boot/dts/rockchip/rockpi-4b-linux.dts / +&i2c7 { / + status = "okay"; / + sht21@40 { / + #address-cells = <1>; / + #size-cells = <0>; / + compatible = "sensirion,sht21"; / + reg = <0x40>; / + }; / +}; / # Update DTB / [CMD] scp arch/arm64/boot/dts/rockchip/rockpi-4b-linux.dtb rock@board_ip:/tmp/ / [Target Board] / [CMD] sudo cp /tmp/rockpi-4b-linux.dtb /boot/dtbs/4.4.154/rockchip/ / [CMD] reboot / # Enable SH21 Driver / [CMD] cd /home/cadtc/rockchip-bsp/kernel / [CMD] make menuconfig / Device Drivers --→ / <*> Hardware Monitoring support --→ / <M> Sensiron humidity and temperature sensors. SHT21 and compat. / [CMD] make modules -j4 / [CMD] scp drivers/hwmon/sht21.ko rock@board_ip:/tmp/ / [Target Board] / [CMD] insmod /tmp/sht21.ko / # Check SH21 Driver / [CMD] lsmod | grep sh21 # Below is sh21 drive installed in target board / sht21 16384 0 / # Enter to HWMON attribution in SysFs / $ cd /sys/class/hwmon/hwmon0/ / # Read temperature value / $ cat temp1_input / # Read humidity value / $ cat humidity1_input / # Schematic / Up Board / Bottom board / # Please to study control_temp from https://github.com/xlloss/embedded_control_app.git

### [6] ISL29023 (Light sensor) Read From SysFS
Read light sensor value
# Modify hw_intfc.conf for enabling i2c7 / [ Target ] / [CMD] vim /boot/hw_intfc.conf / intfc:i2c7=off → intfc:i2c7=on / # Enable ISL29023 Driver / [CMD] cd /home/cadtc/rockchip-bsp/kernel / [CMD] make menuconfig / Device Drivers ---> / [*] Staging drivers ---> / IIO staging drivers --→ / Light sensors --→ / <*> ISL 29018 light and proximity sensor / or / <M> ISL 29018 light and proximity sensor / # modify DTS (rockpi-4b-linux.dts) / [CMD] vim arch/arm64/boot/dts/rockchip/rockpi-4b-linux.dts / +&i2c7 { / + status = "okay"; / + isl29023@44 { / + status = "okay"; / + compatible = "isil,isl29023"; / + reg = <0x44>; / + }; / +}; / # Update DTB / [CMD] scp arch/arm64/boot/dts/rockchip/rockpi-4b-linux.dtb rock@board_ip:/tmp/ / [Target Board] / [CMD] sudo cp /tmp/rockpi-4b-linux.dtb /boot/dtbs/4.4.154/rockchip/ / [CMD] reboot / # 1. if use build-in to kenel. Please update kernel image / # 2. if use module file. Please update isl29018.ko to target board / # Check ISL29023 Driver [module stlye] / [CMD] lsmod | grep isl / # Check ISL29023 Driver [build-in stlye] / [CMD] dmesg | grep isl / # Enter to IIO attribution in SysFs / $ cd /sys/bus/iio/devices/iio:device1 / # Read light value / $ cat in_illuminance0_input / # Schematic / Up Board / Bottom board / # Please to study control_light from https://github.com/xlloss/embedded_control_app.git

### [7] CPU Temperature Read From SysFS
Read CPU Temperature value
# Enter to thermal attribution in SysFs / $ cd /sys/class/thermal / # Read CPU thermal_zone0 value / $ thermal_zone0/temp / # Read CPU thermal_zone1 value / $ thermal_zone1/temp / # Play a H264 file then check CPU temperature / $ gstvideoplay.sh & / $ watch -n 2 "cat thermal_zone0/temp"

### [8] PWM Control From SysFS
1. Control PWM
# Modify hw_intfc.conf for enabling i2c7 / [ Target ] / [CMD] vim /boot/hw_intfc.conf / intfc:pwm0=off → intfc:pwm0=on / intfc:pwm1=off → intfc:pwm1=on / [CMD] cd /sys/class/pwm / $ ls -l / lrwxrwxrwx 1 root root 0 pwmchip0 -> ../../devices/platform/ff420000.pwm/pwm/pwmchip0 / lrwxrwxrwx 1 root root 0 pwmchip1 -> ../../devices/platform/ff420010.pwm/pwm/pwmchip1 / lrwxrwxrwx 1 root root 0 pwmchip2 -> ../../devices/platform/ff420020.pwm/pwm/pwmchip2 / [CMD] cd /sys/class/pwm/pwmchip0/ / # Export PWM1 channel 0 [CMD] echo 0 > export / [CMD] cd pwm0 / # Set a 1KHz for pules / [CMD] echo 1000000 > period / # Set 50% duty cycle for pules / [CMD] echo 500000 > duty_cycle / # Enable PWM / [CMD] echo 1 > enable / # Set a 1Hz for pules / [CMD] echo 1000000000 > period / # Set 25% duty cycle for pules / [CMD] echo 250000000 > duty_cycle / # Change Polarity / [CMD] echo inversed > polarity / [CMD] echo normal > polarity / # Enable PWM / $ echo 1 > enable / # Please to study control_fan from https://github.com/xlloss/embedded_control_app.git / # Please to study control_buzzer from https://github.com/xlloss/embedded_control_app.git