Embedded Linux Camera

---
RockPi4 & Raspberry Pi Camera V2
Raspberry Pi Camera Module 2
IMX219

---
SOC Camera
SOC (RK3399)
ISP
Memory
File
DMA
Image Data
Frame
Buffer
Panel
Camera
CSI-2

---
RK3399 Media Control

---
Media Control
https://opensource.rock-chips.com/wiki_Rockchip-isp1

---
Media Control

---
MIPI CSI-2

---
MIPI CSI-2
Data
Clock
CSI : Camera Slave Interface
CCI : Camera Control Interface
MIPI_Alliance_Specification_for_Camera_S.pdf

---
Multi-Lane Distribution and Merging
Camera
(imx219)

---
Multi-Lane Distribution and Merging
SOC
(RK3399)

---
Multi-Lane Distribution and Merging

---
Low Level Protocol Packet

---
Virtual Channel

---
Line and Frame Blanking

---
ISP

---
Media Control

---
Image Signal Process
- ISP : Image Signal Process
  - Color formation transform
  - De-noising
  - Image Effects
  - Image Resize
  - 3A
    - Auto exposure
    - Auto focus
    - Auto while balance

---
V4L2

---
Video For Linux V2
- V4L2 (Video For Linux V2)
  - Video Device
    - Video capture cards
    - USB webcams
    - Cameras in embedded devices
- Media controller
  - control interface for complex media devices
  - Image pipeline discovery and configuration

---
RK339 Media Control
https://opensource.rock-chips.com/wiki_Rockchip-isp1

---
RK339 Media Control

---
ISP Device Tree

---
Image Sensor Device Tree

---
MIPI CSI-2 Device Tree

---
V4L2 and Camera
/dev/v4l-subdev0
/dev/Video0
Memory
Videobuf2
V4L2-Core
control
V4L2 device
media device
V4L2-SubDevice
Driver
V4L2-Device
Driver
ISP
V4L2_CTL_HANDLE
V4L2_CTL_HANDLE
MIPI-CSI2
I2C
imx219

---
State Machine
user-space
Query Capability
Queue Buffer
Set Formation
Stream on
Set Control
Allocate Buffer

---
V4L2 Video Capabilities
- There are many video formats
  - MPEG, H.264, H.265, YUV, RAW
- The capture device can’t support all of formations
- We have to query device capabilities by
  - VIDIOC_QUERYCAP

---
V4L2 Capabilities & Profiles
/dev/v4l-subdev0
/dev/Video0
VIDIOC_QUERYCAP
V4L2-Core
V4L2-SubDevice
Driver
V4L2-Device
Driver
Support Format Report
ISP
V4L2_CTL_HANDLE
V4L2_CTL_HANDLE
MIPI-CSI2
I2C
imx219

---
V4L2 Videobuf2
- Videobuf2 used to connect user-space and kernel-space
- There are three types Memory Buffer in kernel
  - Physical and virtual address are Not continue
    - videobuf-dma-sg
    - videobuf2-dma-sg
  - Physical address Not continue but virtual address is
    - vmalloc
  - Physical and virtual address are continue
    - DMA

---
V4L2 Videobuf2
- Stream Models
  - USERPTR types
    - The buffers was allocated in userspace
    - It is memory mapped via mmap() ioctl
  - MMAP types
    - https://www.kernel.org/doc/html/v4.8/media/uapi/v4l/func-mmap.html
    - https://www.kernel.org/doc/html/v4.8/media/uapi/v4l/func-munmap.html
  - Read/write access types
    - https://www.kernel.org/doc/html/v4.8/media/uapi/v4l/func-read.html
    - https://www.kernel.org/doc/html/v4.8/media/uapi/v4l/func-write.html
  - DMABUF types

---
V4L2 Queue and Dqueue Buffer
Exchange a buffer with the driver
Applications call the  VIDIOC_QBUF ioctl to enqueue an empty (capturing) or
filled (output) buffer in the driver's incoming queue.
Applications call the VIDIOC_DQBUF ioctl to dequeue a filled (capturing) or displayed (output) buffer from the driver's outgoing queue
VIDIOC_DQBUF
VIDIOC_QBUF
Application
out going
In coming
Image Data
Frame 1
...
Frame n
Frame 1
...
Frame n

---
V4L2 Video Stream
- Need to implement the streaming hooks
- Addresses two things:
  - Memory Management: Buffer allocation, queuing and dequeuing
  - Streaming control
Application
RAM
SOC
Camera
I2C
Supporting_the_Camera_Interface.pdf

---
V4L2 Control
- Adjust parameter for Image quality
  - 3A (AE, AF, AWB)
    - ISP
    - Image sensor
- IOCTL
- v4l2-utilities
3A
I2c control
IO control
RAM
SOC
ISP
Camera

---
V4L2 Sub-device

---
V4L2_Subdev
Capture
Control
Application
yavta
v4l2-utilities
Video Device
Sub Device
RAM
SOC
Camera
I2C

---
V4L2_Subdev
- Many capture drivers need to communicate with sub-devices
  - For webcams common sub-devices
    - Mic
    - Camera
    - LED
- v4l2_subdev struct (v4l2-subdev.h) represent a sub-device

---
Sub-device Model
file:///home/slash/work/for_cadtc/rockpi4-b/rockpi-kernel/include/media/v4l2-subdev.h

---
Camera Sub-device
- Camera
  - Controller
  - Image Sensor
- Sony IMX219
sub-device
IMX219
Application
RAM
SOC
Camera
I2C

---
IMX219
https://www.electronicsdatasheets.com/download/5721ed8ce34e24fd697a913a.pdf

---
IMX219
https://www.electronicsdatasheets.com/download/5721ed8ce34e24fd697a913a.pdf

---
IMX219 DTS

---
IMX219 Driver
GPIO
Power control

---
IMX219 Driver
Initial
sub-device ops
Create
sub-device node
Medial control
initial
sub-device
register

---
IMX219 Driver
Stream
Control
Power
Control
Media
Control

---
IMX219 Driver
V4l2 control
initial

---
IMX219 Driver
Initial IMX291 Table1
MCLK:24MHz 3280x2464 21.2fps MIPI LANE2

---
IMX219 Driver
Initial IMX291 Table2
MCLK:24MHz 1920x1080 30fps MIPI LANE2

---
Enable Camera Video
- Enable Camera Module for RockPi4
  - Change /boot/hw_intfc.conf:
    - intfc:dtoverlay=imx219
- Open Video
  - gst-launch-1.0 v4l2src device=/dev/video0 io-mode=4 ! videoconvert ! autovideosink

---
Capture Image
- Yavta
  - Yet Another V4L2 Test Application
  - https://git.ideasonboard.org/git/yavta.git/
- Getting supported controls/formats/resolutions:
  - yavta -l --enum-formats --enum-inputs /dev/video0
- Capturing 10 frames on the disk
  - yavta -F /dev/video0 --capture=10

---
Image View
- Gstreamer
  - gst-launch-1.0 v4l2src device=/dev/video1 io-mode=4 ! videoconvert ! video/x-raw,format=NV12,width=640,height=480 ! autovideosink
- Vooya
  - https://www.offminor.de/

---
v4l2-utils
- Get video format
  - v4l2-ctl -d /dev/video0 -V
- List ctrls menus
  - v4l2-ctl -d /dev/video0 -L
  - v4l2-ctl -d /dev/video0 -l
- Set the value of the controls
  - v4l2-ctl -d /dev/video0 --set-ctrl gain=150
- Help
  - v4l2-ctl --help-all