DRM / KMS

---
DRM
- Direct Rendering Manager
  - Management of buffers and free space within that memory.
  - Solve Frame buffer driver cannot be used GPU and multi-user process.

---
DRM
- DRM consists of
  - KMS : Kernel Mode Setting
    - Change resolution and depth
  - DRI : Direct Rendering Infrastructure
    - Interfaces to access hardware directly
  - GEM : Graphics Execution Manager
    - Buffer management
  - DRM Driver in kernel side
    - Access hardware

---
DRM
If no use DRM

---
DRM
Use DRM

---
FBDEV
The frame buffer device provides an abstraction for the graphics hardware.
Application
User Space
memory
MMAP
memory
Kernel Space
FB Driver

---
V4L2
- Video For Linux 2
  - Multimedia, Video-In
  - Rotator and Scaler
  - Video codec

---
KMS
- KMS device model
  - CRTCs
  - Connectors
  - Encoders
  - Planes
- Kernel Mode Setting
  - screen resolution
  - color depth and
  - refresh rate

---
KMS
- linux-4.20.7/drivers/gpu/drm/
- linux-4.20.7/drivers/gpu/drm/exynos
exynos_drm_crtc.c
exynos_drm_dpi.c
exynos_drm_drv.c
exynos_drm_dsi.c
exynos_drm_fb.c
exynos_drm_fbdev.c
exynos_drm_fimc.c
exynos_drm_fimd.c
exynos_drm_g2d.c
exynos_drm_gem.c
exynos_drm_gsc.c
exynos_drm_iommu.c
exynos_drm_ipp.c
exynos_drm_mic.c
exynos_drm_plane.c
exynos_drm_rotator.c
exynos_drm_scaler.c
exynos_drm_vidi.c
exynos_hdmi.c
exynos_mixer.c

---
KMS
exynos4412-tiny4412.dts
&fimd {
pinctrl-0 = <&lcd_clk &lcd_data24>;
pinctrl-names = "default";
samsung,invert-vden;
samsung,invert-vclk;
display-timings {
native-mode = <&timing0>;
timing0: timing {
clock-frequency = <33000000>;
hactive = <800>;
vactive = <480>;
hfront-porch = <90>;
hback-porch = <10>;
hsync-len = <28>;
vback-porch = <29>;
vfront-porch = <13>;
vsync-len = <3>;
vsync-active = <0>;
hsync-active = <0>;
pixelclk-active = <0>;

---
KMS
Encode
Connecter
CRTC
FrameBuffer
Planes

---
LCD Parameters
- VBPD : vertical back porch
- VFBD : vertical front porch
- VSPW : vertical sync pulse width
- HBPD : horizontal back porch
- HFPD : horizontal front porth
- HSPW : horizontal sync pulse width

---
LCD Display Parameters
- Dotclock
  - The video hardware draws pixels on the display speed
dotclock = (X-resolution + left margin + right
        Margin + HSYNC length) *
        (Y-resolution + upper margin + lower margin + VSYNC length) * refresh rate
pixclock = 1/dotclock

---
LCD Display Parameters

---
LCD Display Parameters

---
LCD Display Parameters

---
Tiny4412 LCD

---
Tiny4412 LCD

---
Tiny4412 LCD

---
Tiny4412 LCD

---
static int exynos_dpi_parse_dt(struct exynos_dpi *ctx)
{
[...]
np = of_get_child_by_name(dn, "display-timings");
if (np) {
struct videomode *vm;
int ret;
of_node_put(np);
[…]
ret = of_get_videomode(dn, vm, 0);
if (ret < 0) {
devm_kfree(dev, vm);
return ret;
}
[...]
return 0;
}