Input Subsystem

---
Input Subsystem
Qt
Weston
Xwindow
User-space
/dev/input/eventX
Input Core
Input Device Driver
Input Event Driver
Bus Driver (serial, i2c, spi, USB ...)
kernel-space
Device (keyboard, button, mouse ...)
Hardware

---
Input Subsystem
- Documentation/input
- Documentation/input/event-codes.txt
- Mouse, keyboard, button, joystick ...
- /dev/input
  - event0, event1, event2 …
  - mouse0 …
  - misc0 ...

---
How to Check Input Event
[CMD] cat /dev/input/event1 | hexdump -C
[CMD] evtest cat /dev/input/event1

---
Input Device Driver

---
Input Device Driver
- The input protocol uses a map of types and codes
  to express input device values to user-space
- $(KERNEL)/drivers/input
  - input.c, evdev.c
  - drivers/input/keyboard/
    - gpio_keys.c
    - gpio_keys_polled.c
    - simple_keys.c
  - drivers/input/touchscreen/
    - edt-ft5x06.c

---
Input device Event and Key code
- include/uapi/linux/input.h
- include/uapi/linux/input-event-codes.h
- Event Types
  - EV_KEY
  - EV_ABS …
- Keys Codes
  - KEY_ESC
  - KEY_1
  - KEY_BACKSPACE ...

---
Event Structure
rockpi-kernel/include/uapi/linux/input.h

---
Event Types - Code
- EV_SYN
  - Used as markers to separate events
- EV_KEY
  - Used to describe state changes of KEY
    - keyboards, buttons
    - or other key-like devices
- EV_ABS
  - Used to describe absolute axis value changes
    - touchscreen

---
Event Types - Code
- EV_SYN
  - SYN_REPORT
    - Used to synchronize and separate events into
      packets of input data changes occurring at the
      same moment in time
  - SYN_MT_REPORT
    - Used to synchronize and separate touch
      events. See the multi-touch-protocol.txt
      document for more information

---
Event Types - Code
- EV_KEY
  - EV_KEY events take the form
    - KEY_<name> or BTN_<name>
    - For example : KEY_A
  - BTN_TOUCH
    - used for touch contact

---
Key - Code
#define KEY_R 19
#define KEY_T 20
#define KEY_Y 21
#define KEY_U 22
#define KEY_I 23
#define KEY_O 24
#define KEY_P 25
#define KEY_A 30
#define KEY_S 31
#define KEY_F1 59
#define KEY_F2 60
#define KEY_F3 61
#define KEY_RESERVED 0
#define KEY_ESC 1
#define KEY_1 2
#define KEY_2 3
#define KEY_3 4
#define KEY_4 5
#define KEY_5 6
#define KEY_6 7
#define KEY_7 8
#define KEY_8 9
#define KEY_9 10
#define KEY_0 11

---
Input Driver API
Allocate managed input device
struct input_dev *devm_input_allocate_device(struct device *dev)
Register device with input core
int input_register_device(struct input_dev *dev)
Report new input event
void input_event(struct input_dev *dev,
unsigned int type, unsigned int code, int value)

---
Input Driver API
Report new input event
static inline void input_sync(struct input_dev *dev)
{
input_event(dev, EV_SYN, SYN_REPORT, 0);
}
void input_event(struct input_dev *dev,
unsigned int type, unsigned int code, int value)

---
Input Driver API
simple_key
Allocate managed input device

---
Input Driver API
Register device with input core

---
Input Driver API
Report new input event

---
simple_keys

---
simple_keys.c
$(KERNEL)/driver/char/simple_keys.c

---
simple_keys.c

---
simple_keys.c - DTS
Physical GPIO-Key

---
simple_keys.c
static int simple_key_probe(struct platform_device *pdev)
{
int ret, i;
char dt_gpio_name[15];
struct input_dev *input;
struct device *dev = &pdev->dev;
input = devm_input_allocate_device(dev);
if (!input) {
dev_err(dev, "failed to allocate input device\n");
return -ENOMEM;
}
Alloc a input device

---
simple_keys.c
input->name = pdev->name;
input->phys = "sample-keys/input0";
input->dev.parent = dev;
input->open = simple_keys_open;
input->close = simple_keys_close;
input->id.bustype = BUS_HOST;
input->id.vendor = 0x0001;
input->id.product = 0x0001;
input->id.version = 0x0100;
input_set_capability(input, EV_KEY, BTN_0);
simple_key.key_type = EV_KEY;
simple_key.key_code[0] = BTN_0;
Key Code Map

---
simple_keys.c
for (i = 0; i < GPIO_NUM; i++) {
simple_key.irq[i] = 0;
sprintf(dt_gpio_name, "key%d", i);
simple_key.gpiod[i] = devm_gpiod_get_optional(&pdev->dev,
dt_gpio_name, GPIOD_IN);
...
simple_key.irq[i] = gpiod_to_irq(simple_key.gpiod[i]);
ret = devm_request_irq(&pdev->dev, simple_key.irq[i],
gpio_irq_isr, IRQ_TYPE_EDGE_BOTH, "key-irq", &simple_key.irq[i]);
        …
disable_irq_nosync(simple_key.irq[i]);
}
Key Interrupt
Setting

---
simple_keys.c
ret = input_register_device(input);
if (ret) {
dev_err(dev, "Unable to register input device, error: %d\n",
ret);
return ret;
}
for (i = 0; i < GPIO_NUM; i++) {
if (simple_key.irq[i])
enable_irq(simple_key.irq[i]);
}
Register device
with input core

---
simple_keys.c
static irqreturn_t gpio_irq_isr(int irq, void *devid)
{
int *gpio_irq_num, i;
unsigned char keyval;
gpio_irq_num = (int *)devid;
for (i = 0; i < GPIO_NUM; i++) {
if (irq == simple_key.irq[i])
break;
}
keyval = gpiod_get_value(simple_key.gpiod[i]);
keyval = ~keyval & 0x01;
pr_err("keyval %d\r\n", keyval);
input_event(simple_key.input, simple_key.key_type,
simple_key.key_code[i], keyval);
input_sync(simple_key.input);
return 0;
}
Report new
input event

---
gpio_keys_polled

---
gpio_keys_polled and DTS
drivers/input/keyboard/gpio_keys.c
Key Code

---
gpio_key.c
User-space
/dev/input/eventX
/sys/class
ISR
GPIO INT
Input core
Input core
GPIO driver
Report key
event
work-queue
kernel-space
hardware
Button

---
Input Subsystem - Test
- From SysFS
  - # ls -l /sys/class/input/ -l
Use gpio-keys Driver

---
Input Subsystem – Test 2
- From Interrupt
  - # watch -n 1 "cat /proc/interrupts | grep User "
Use gpio-keys Driver
IRQ Trigger
IRQ Device

---
Input Subsystem – Test 3
- Use evtest
  - [CMD] evtest /dev/input/event1
Use gpio-keys Driver