SPI Drivers

---
SPI Protocol - 1
- Serial Peripheral Interface (SPI)
  - synchronous serial communication
  - Signals
    - SCK (clock)
    - SS (chip select)
    - MISO (Data-In)
    - MOSI (Data-Out)
SPI
https://en.wikipedia.org/wiki/Serial_Peripheral_Interface

---
SPI Protocol - 2
- SPI Mode
  - CPOL determines the polarity of the clock
    - CPOL=0 is a clock which idles at 0, and fetch data at pulse of 1
    - CPOL=1 is a clock which idles at 1, and fetch data at pulse of 0
  - CPHA determines the timing of the data bits relative
    to the clock pulses
    - For CPHA=0,
      - 1. data on the trailing edge of the clock cycle
      - 2. captures the data on the leading edge of the clock cycle
    - For CPHA=1,
      - 1. data on the leading edge of the clock cycle
      - 2. captures the data on the trailing edge of the clock cycle
https://en.wikipedia.org/wiki/Serial_Peripheral_Interface#/media/File:SPI_timing_diagram2.svg

---
SPI Host
- SPI Host driver
  - rockpi-kernel/drivers/spi/
    - spi.c
    - spidev.c
    - spi-rockchip.c
    - Spi-gpio.c
SPI Device Tree
Node
PinMux

---
SPI Host - GPIO
- SPI Host Driver – GPIO
  - rockpi-kernel/drivers/spi/spi-gpio.c
DTS

---
SPI Host - GPIO
DTS

---
Spidev – User Space Control
- drivers/spi/spidev.c
- include/linux/spi/spidev.h
- Documentation/spi/
  - spidev
- character device
  - major number 153
  - /dev/spidev1.0
  - sys/class/spi_master/spi1
  - /sys/class/spidev/spidev1.0

---
SPI Driver - 1
spidev_tool
User space
/dev/spidev1.0
Kernel space
spi.c
spidev.c
SPI drivers
spi-rockchip.c
Hardware
Device

---
SPI Driver - 2
Application
User space
/dev/mtdblock
Kernel space
MTD drivers
SPI drivers
spi.c
spidev.c
MTD
spi-rockchip.c
SPI Nor-Flash Driver
Hardware
SPI Nor-Flash

---
SPI Driver – SPI Model
$KERNEL/include/linux/spi/spi.h

---
SPI Driver – spi.c
- SPI stack core
- Export SPI kernel API
- Construct SPI subsystem

---
SPI Driver – spi-rockchip.c
- SPI bus implement in SOC
- Register for spi.c
- Communication with SPI device
Up-Layer
spi-rockchip.c
Driver
Hardware
Device

---
SPI Driver – spi-dev.c
- Register a SPI character driver
- Use SPI kernel API to control SPI device
- Convenient implement user-space driver
User space
/dev/spidev1.0
Kernel
Character Core
spidev.c
spi.c

---
Spidev – User Space Control
- spidev_tool
  - https://github.com/xlloss/spidev_tool
spidev_tool
User space
/dev/spidev1.0
Kernel space
SPI Driver
Hardware
Device

---
Spidev – User Space Control
spidev_tool
User space
/dev/spidev1.0
Kernel space
spi.c
spidev.c
SPI drivers
spi-rockchip.c
Hardware
Device

---
Spidev – User Space Control

---
W25Q128 SPI Flash
MOSI
MISO
RK3399
SCLK
SS
https://www.winbond.com/resource-files/w25q128fv%20rev.l%2008242015.pdf

---
W25Q128 SPI Flash - ID
Device ID and Instruction Set Table

---
W25Q128 SPI Flash - ID
Device ID and Instruction Set Table

---
W25Q128 SPI Flash - ID
Read JEDEC ID Instruction - SPI Mode

---
Exercise - 1
- Read ID with spidev_tool
- For example
  - ./spdev_tool -D /dev/spidev1.0 -s 10000 -p "\x9F\x00\x00\x00" -v

---
Exercise - 2
- Add a MTD Nor-Flash driver
- Read, write, mount, umount MTD block device
  - $ mount /dev/mtdblock2 /tmp/mtd_device/
  - $ touch /tmp/mtd_device/test_file
  - $ umount /dev/mtdblock2

---
MTD Subsystem – spi-nor
- drivers/mtd/
- drivers/mtd/spi-nor
  - spi-nor.c
- drivers/mtd/devices
  - m25p80.c
DTS

---
MTD Subsystem – spi-nor