CH9 Control Hardware Driver

---
Application and Hardware
Application
Library
C library
System Call
User Space
Device Driver
Linux kernel
Kernel Space
Hard ware

---
User Space and Kernel Space
Test Application
User Space
Device Node
Linux Char Driver
Kernel Space
Hardware
Device

---
SysFS
- Allows kernel code to export information to user processes
- SysFS is an in-memory file system
- It provides two components
  - A kernel programming interface for exporting these items via sysfs
  - User interface to view and manipulate these items that maps back to the kernel objects which they represent

---
LED and SysFS
User-space
SysFS
Kernel-space
LED Driver
led-triggers.c
led-class.c
Trigger driver
switch
led-core.c
leds-gpio.c
led driver
Hardware
LED

---
Sys File System
# tree -L 1 /sys/
# tree -L 1 /sys/class/i2c-dev/i2c-0/
# tree -L 1 /sys/class/i2c-dev

---
LED Drivers

---
LED Schematic
GPIO3_D4/I2S0_SDI1SDO3_d → LED1
GPIO3_D5/I2S0_SDI2SDO2_d → LED2

---
LED Subsystem
- Control LED convenient with SysFS
  - For example
    - echo 1 > /sys/class/leds/user-led2/shot
- Switch different LED trigger type in SysFS
  - For example
    - echo "gpio" > /sys/class/leds/user-led2/trigger
    - echo "1" > /sys/class/leds/user-led2/brightness
    - echo "0" > /sys/class/leds/user-led2/brightness

---
LED SysFS
Check trigger type
Switch trigger type

---
GPIO Control

---
Driver LED in User Space
- Paths in Sysfs
- /sys/class/gpio:
  - Control interfaces used to get userspace control over GPIOs;
  - GPIOs themselves
  - GPIO controllers("gpio_chip" instances)
/sys/class/gpio/
  - "export" : ask the kernel to export GPIO to userspace by writing
    - "echo 19 > export"
    - create a "gpio19" node in /sys/class/gpio
  - "unexport" : Reverses the effect of exporting to userspace
    - "echo 19 > unexport"
    - remove "gpio19" node from /sys/class/gpio

---
Cadtc Ext Board LED

---
RockPi4B HEAD

---
PWM Sub System

---
PWM
PWM : Pulse Width Modulation
https://circuitdigest.com/tutorial/what-is-pwm-pulse-width-modulation

---
PWM
https://en.wikipedia.org/wiki/Pulse-width_modulation

---
PWM Parameter in Linux
Period
  - The total period of the PWM signal
  - Value is in nanoseconds
  - sum of the active and inactive time of the PWM
duty_cycle
  - The active time of the PWM signal
  - Value is in nanoseconds
  - must be less than the period.

---
PWM Parameter in Linux
- Polarity
  → The polarity of the PWM signal
- Enable
  → Enable PWM Signal

---
PWM Driver
- $(KERNEL_SRC)/Documentation/pwm.txt
- Platform Driver
  - drivers/pwm/
  - drivers/pwm/core.c
  - drivers/pwm/pwm-rockchip.c

---
PWM Subsystem
Application 1
Application 2
User Space
/sys/class/pwm
/dev/dev-mg996rs
Kernel Space
core.c
cadtc_mg996r.c
Callback implement
and register
pwm-rockchip.c
MG996R

---
RockPi4B HEAD

---
PWM SYSFS
/sys/class/pwm/pwmchip0
device export npwm power subsystem uevent unexport
echo 0 > export
capture enable polarity uevent duty_cycle period power
echo “20000000” > period
//20ms, 50 Hz
//2ms
echo "2000000" > duty_cycle
//Enable
echo 1 > enable

---
Hwmon Subsystem

---
Hwmon Subsystem
User
SysFS
attr_show
Hwmon.c
attr_store
Hwmon driver
Kernel
Hwmon driver
Hardware

---
SHT21
- Simple interface
- Bus interface
  - I2C, GPIO, SPI
Sensors
  - Temperature
  - Voltage
  - Humidity
  - Fan speed
  - PWM control

---
SHT21
SHT21
RockPi4B

---
SHT21
Hold master communication sequence
No Hold master communication sequence

---
SHT21
I2C
I2C

---
SHT21
Hwmon Sysfs
# ls /sys/class/hwmon/hwmon0
device name subsystem uevent
humidity1_input power temp1_input
temperature
# cat /sys/class/hwmon/hwmon0/temp1_input
32279
humidity
# cat /sys/class/hwmon/hwmon0/humidity1_input
34512