U-boot

---
Bootloader
- What is bootloader
- Boot : short bootstrap
  - Initialize basic of SOC (CPU, RAM, CLK)
  - BL1, BL2
Loader
  - Load OS to RAM(DDR) form storage
  - u-boot

---
Different Embedded Linux bootloader
- U-boot
- UEFI
- Redboot
- Stubby (Linaro) …
- Anyway, they are same target
  - Load and boot OS to RAM from storage

---
Concepts of the Boot Loader
- Boot Loader is varied from CPU to CPU,from board to board.
- All the system software and data are stored in some kind of nonvolatile memory.
- Operation Mode of Boot Loader
  - Boot : Initialize basic of SOC
  - Load : load OS to RAM then execute

---
RK3399 SOC
http://wiki.friendlyarm.com/wiki/index.php/NanoPi_M4#Diagram.2C_Layout_and_Dimension

---
Embedded Linux System Booting
Boot
Initialize HW
Loader
Load OS to memory
OS initial / load driver
Linux
DTB
RootFS
OS running

---
RockPi4 Image Partition
partmap.txt – Image layout in SD card
Loader
idbloader.img
0x8000,0x280000
u-boot
Uboot.img
0x800000,0x0400000
Trust
Trust.img
0xC00000,0x0400000
Linux kernel
Linux kernel
SD Card Part List 4
RootFS
rootfs.img
SD Card Part List 5

---
Boot
Power On BootROM code (work in cache)
  - Load BL1
BL1 (work in cache)
  - Initial simple exception vectors, PLL (clock)
  - Initial Multi-CPU
  - Load BL2
BL2 (work in cache)
  - Initial DDR memory
  - Initial C environment (stack, heap, )
  - Load BL31

---
Boot
BL31 (work in DDR)
  - Initial exception vectors
  - Load BL32 (u-boot)
BL32 U-boot
  - Initial storage device
  - Load Linux Kernel
Kernel
  - kernel/Documentation/arm64/booting.txt
  - Mount RootFS

---
Introduce U-boot

---
U-boot
- Das U-Boot -- the Universal Boot Loader
- http://www.denx.de/wiki/U-Boot
- GitHub for u-boot
- Open Source follow GPL
- Supply many CPU
  - PPC, ARM, x86, MIPS, AVR32 …
Supply basic periphery devices
  - UART, Flash, SD/MMC ….

---
u-boot directory structure
- Arch → Many types CPU : Arm, mips, i386 ...
- Board → Many types develop board : Samsung, ti, davinci ...
- Tools → Make Image (u-boot, linux ) or S-Record image tool
- Drivers → Some HW control code
- FS → Supply file system : fat, jffs2, ext2, cramfs
- Disk→ Supply disk driver and partition handling
- Common → Major command and relation environment setting
          source code

---
u-boot directory structure about
rk3399
arch/arm/cpu/armv8/
  - ARMv8 relate
arch/arm/cpu/armv8/rk33xx/
  - rk3399 related
  - Clock, i2c, irom, mmc, emmc ...
board/rockchip/rk33xx/
  - Board level related
  - Peripheral initial

---
Rk3399 Configure File
- Cmd/
  - u-boot command related
- Configures/
  - High Level Define
    - rock-pi-4b-rk3399_defconfig
- include/configs/
  - Low Level Define
    - config_distro_bootcmd.h
    - evb_rk3399.h
    - rk3399_common.h

---
How to Build u-boot
- Easy Build :
  [CMD] git clone --recursive https://github.com/radxa/rockchip-bsp.git
  [CMD] cd ./rockchip-bsp
  [CMD] ./build/mk-uboot.sh rockpi4b
- Clear :
  [CMD] make distclean
- Configure :
  [CMD] make rock-pi-4b-rk3399_defconfig
- Build :
  [CMD] make -j4
- Create Image :
  [CMD] cd rockchip-bsp/rkbin/tool/
  [CMD] loaderimage --pack --uboot ../../u-boot/u-boot-dtb.bin /uboot.img

---
U-boot Configure (1)
Change u-boot about
  - Add Command
  - Modify boot parameter
  - Add Function

---
U-boot Configure (2)
- Edit Configure
- Method 1
  - menuconfig
    - [cmd] make menuconfig
Method 2
  - Edit configure file
    - config_distro_bootcmd.h
    - evb_rk3399.h
    - rk3399_common.h

---
U-boot Common Function

---
Help
- help
  → print command description/usage
- $ help
  → help mm
- $ ?
=> help mm
mm - memory modify (auto-incrementing address)
Usage:
mm [.b, .w, .l, .q] address
=>

---
md
md
→ memory display
→ md [.b, .w, .l, .q] address [# of objects]

---
mw
mw
→ memory write
→ mw [.b, .w, .l, .q] address value [count]

---
mmc
mmc list
→ lists available devices

---
mmc
mmc info
→ display info of the current MMC device

---
mmc
mmc part
→ lists available partition on current mmc device

---
mmc
mmc dev
→ show or set current mmc device [partition]
→ mmc dev [dev] [part]

---
FAT List
fatls
→ list files in a directory
→ fatls <interface> [<dev[:part]>] [directory]
    - list files from 'dev' on 'interface' in a 'directory'

---
FAT Load
fatload
→ fatload - load binary file from a FAT filesystem
→ fatload <interface> [<dev[:part]> [addr [filename [bytes [pos]]]]]
    load binary file 'filename' from 'dev' on 'interface'
    to address 'addr' from fat filesystem
=> fatload mmc 1:4 ${kernel_addr_r} vmlinuz-4.4.154
reading vmlinuz-4.4.154
20371464 bytes read in 858 ms (22.6 MiB/s)
=> fatload mmc 1:4 ${fdt_addr_r} dtbs/4.4.154/rockchip/rockpi-4b-linux.dtb
reading dtbs/4.4.154/rockchip/rockpi-4b-linux.dtb
94603 bytes read in 15 ms (6 MiB/s)
=> fatload mmc 1:4 ${ramdisk_addr_r} initrd.img-4.4.154
reading initrd.img-4.4.154
5038020 bytes read in 215 ms (22.3 MiB/s)

---
printenv
printenv
→ print environment variables
→ printenv name

---
setenv
- saveenv
- setenv
  → set environment variables
  → setenv name value

---
Simple Script
Script
LED Blank

---
run
run
→ run commands in an environment variable
→ run var [...]
=> run bootcmd
switch to partitions #0, OK
mmc1 is current device
Scanning mmc 1:4...
Found /extlinux/extlinux.conf
pxefile_addr_str = 0x00500000
bootfile = /extlinux/extlinux.conf
Retrieving file: /extlinux/extlinux.conf
reading /extlinux/extlinux.conf
1646 bytes read in 5 ms (321.3 KiB/s)
select kernel
1:	kernel-4.4.154
2:	kernel-4.4.154-999-rockchip-gcfa47f25e
3:	kernel-4.4.154-113-rockchip-gdb9dfc2cdd25
4:	kernel-4.4.154-00039-g00fccd3
5:	kernel-4.4.154
Enter choice: Retrieving file: /hw_intfc.conf
reading /hw_intfc.conf
1968 bytes read in 4 ms (480.5 KiB/s)
command

---
booti
booti
→ booti - boot Linux kernel 'Image' format from memory
→ booti [addr [initrd[:size]] [fdt]]

---
Boot Linux kernel

---
System Start Up
ROM Code@RK3399
Read IDB_Loader
Put IDB_Loader to
SRAM
Initial PLL
Initial DDR
Load BL31

---
System Start Up
Load BL31
Init C Environment
Init Periphery
Load U-Boot
Load Linux Image
To DDR
Load Linux DTB
BOOT Linux Kernel

---
Boot Linux Kernel Command
bootcmd
  - Power On will auto run content of bootcmd
[CMD] printenv bootcmd
bootcmd=run distro_bootcmd;boot_android ${devtype} ${devnum};bootrkp;

---
Boot OS (Linux) Command
- booti
  → boot Linux kernel 64 bit standard kernel image
- boota
  → boot android style kernel image
- Boot command
  → booti [Kernel image addr] [RAM disk adr ] [DTB addr]
  → $ booti kernel_addr ramdisk_addr DTB_addr

---
Linux Kernel Command (bootargs)
bootargs
  - $ printenv bootargs (Linux kernel command)
  - earlycon : earlay console device
  - console : Linux console device
  - root : RootFS device
- Enter Linux kernel to check
  - $ cat /proc/cmd
earlyprintk console=ttyFIQ0,1500000n8 rw init=/sbin/init rootfstype=ext4 rootwait root=UUID=a54358ce-55c2-4f4f-bf6d-7106997cfb8f console=ttyS2,1500000n8

---
How to jump to kernel
- Use boot command
  → cmd/cmd_booti.c
- Jump to Linux kernel
  → arch/arm/lib/bootm.c
  → boot_os_fn *bootm_os_get_boot_func(int os)
  → int do_bootm_linux(int flag, int argc, char *const argv[],
          bootm_headers_t *images)
  → void (*kernel_entry)( void *fdt_addr,
          void *res0,
          void *res1,
          void *res2);

---
Add Function to Board Setting File

---
evb-rk3399.c
- board/rockchip/evb_rk3399/evb-rk3399.c
- Add function to here
diff --git a/board/rockchip/evb_rk3399/evb-rk3399.c b/board/rockchip/evb_rk3399/evb-rk3399.c
index 8e3fce4aa4..e5b4041288 100644
--- a/board/rockchip/evb_rk3399/evb-rk3399.c
+++ b/board/rockchip/evb_rk3399/evb-rk3399.c
@@ -30,6 +30,11 @@ int rk_board_init(void)
        struct udevice *pinctrl, *regulator;
        int ret;
+ printf("%s\n", __func__);
+
+ /* user2 led power-off */
+ run_command("gpio clear 125", 0);
+
        /*
        * The PWM does not have decicated interrupt number in dts and can
        * not get periph_id by pinctrl framework, so let's init them here.

---
New a Command

---
Add Feature
- Add command → cmd/
- Add driver → driver/
- Add application → example/

---
Add Command
- How to create a command ?
- Directory
  - cmd/ → booti.c , mmc.c, mem.c ...
U_BOOT_CMD(name,maxargs,rep,cmd,usage,help)
  - include/command.h

---
How to Command
cmd/cmd_version.c
 Include/command.h
#define U_BOOT_CMD(_name, _maxargs, _rep, _cmd, _usage, _help)

---
Hello World Command

---
Hello World Command
cmd/Makefile

---
Hello World Command
cmd/Kconfig