Linux Kernel

---
Linux kernel key features
- Portability and hardware support
- Scalability
- Compliance to standards and interoperability
- Exhaustive networking support
- Stability and reliability
- Modularity
- Easy to program.

---
Linux Kernel in the System
Application
…..
Application
…..
Library
Library
C Library
User Space
System Call
Linux Kernel
Kernel Space
Hardware

---
Linux Kernel

---
Kernel Source
- https://www.kernel.org/
- Many chip vendors
- kernel sub-communities
  - Architecture communities
    - ARM, MIPS, PowerPC ...
  - device drivers communities
    - I2C, SPI, USB, PCI, network ...

---
Programming language
- Implemented in C like all Unix systems
- A little Assembly is used too
- No C++ used
- No C library
- No floating point computation
- Kernel code has to supply its own library implementations
  - X : printf(), memset(), malloc(),...
  - O: printk(), memset(), kmalloc()

---
Linux Sources Important Folder
Kernel Image
  - arch/<ARCH>/boot/
  - Arch/arm64/boot
DTS
  - arch/<ARCH>/boot/dts
  - Arch/arm64/boot/dts/rockchip/
- driver/
- Documentation/

---
Kernel Basic Command

---
Basic Build Command
$ make
  - Build all
$ make dtbs
  - Build Device-tree only
$ make modules
  - Build kernel modules only
$ make modules_install
  - Install all modules to folder

---
Basic Build Command
- [CMD] make deb-pkg
  - Build both source and binary deb kernel packages
- [CMD] make modules_install
  - Install all modules to INSTALL_MOD_PATH
- [CMD] make mrproper
  - Remove all generated files (.config)
- [CMD] make clean
- [CMD] make distclean
  - Remove editor backup and patch reject files

---
Make Help
[CMD] make help

---
Linux System Memory Layout

---
Physical and Virtual Memory
Physical
Address
Virtual
Address
32 Bit CPU

---
Virtual Memory Organization
AArch64 Linux memory layout with 4KB pages + 3 levels
64 Bit CPU
512GB
reserved for
kernel-space
512GB
reserved for
user space

---
Linux Process Memory
Kernel
Kernel Space
512G
Stack
Mmap Region
User Space
512G
Heap
.bss
.data
.text

---
Linux Process Memory
Kernel
Space
Kernel
Space
Kernel
Space
Kernel
Space
User
Space
User
Space
User
Space
User
Space
Process 1
Process 3
Process 3
Process 2

---
How to Build Linux Kernel

---
Specifying Cross-compilation
- make ARCH=arm64 CROSS_COMPILE=arm-linux- …
  → [CDM] export ARCH=arm64
  → [CMD] export CROSS_COMPILE=aarch64-linux-gnu-
- Add above setting to script
  → [CMD] source $PATH/set_toolchain.sh

---
set_toolchain.sh
export PATH=/home/cadtc/host_share_folder/toolchain/gcc-linaro-7.3.1-2018.05-x86_64_aarch64-linux-gnu/bin/
# Toolchain path add to environment variable
export ARCH=arm64
# Set SOC architecture type
export CROSS_COMPILE=aarch64-linux-gnu-
#Set compile prefix name
export KERNELDIR=/home/cadtc/rockchip-bsp/kernel
#Set Linux kernel source path

---
Predefined Configuration Files
- Default configuration
  → arch/<arch>/configs/
- Use RockPi4 default Configure
  → [CMD] make rockchip_linux_defconfig
- To create your own default configuration file
  → [CMD] make savedefconfig, to create a minimal configuration file
  → [CMD] mv defconfig arch/arm64/configs/myown_defconfig

---
Kernel Compilation
Build kernel Image
→ [CMD] make -j4
→ To run multiple jobs in parallel if you have multiple CPU cores
Generates Image
  - arch/arm64/boot/Image
    → Image for ARM64,
  - arch/arm64/boot/dts/rockchip/
    → DTB : rockpi-4b-linux.dtb

---
Kernel Configuration
Kernel source
Image
rockchip_linux_defconfig
Network , File System,
Device Driver, HW SPEC ...
?

---
Kernel Configuration
Configure Kernel
menuconfig
Make Kernel
Kernel source code
DTS
Output Kernel
Image
DTB
modules

---
How to Select Feature in Kernel

---
Kernel Configuration
- The kernel configuration and build system is based on multiple Makefiles
- The configuration is stored in the .config file at the root of kernel sources
- As options have dependencies, typically never edited by hand, but through graphical or text interfaces
  - [CMD] make menuconfig → Text
  - [CMD] make xconfig → graphical

---
Kernel Configuration
.config
${KERNEL}/arch/arm64/configs/
rockchip_linux_defconfig

---
Kernel or Module?
- The kernel image is a single file, resulting from the linking of all object files that correspond to features enabled in the configuration
- Some features (device drivers, file-system, etc.) can however be compiled as modules

---
Menuconfig

---
menuconfig

---
Kernel Configuration Options

---
Configuration
make menuconfig
.config
make
../include/generated/autoconf.h
Makefile
module

---
Corresponding .config File Excerpt
.config
$(KERNEL_PATH)/drivers/i2c/buses/
Makefile

---
Check CONFIG Setting
- In Kernel Source
  - [CMD] cat .config | grep ${CONFIG_NAME}
- In Run Time Environment
  - [CMD] cat /proc/config.gz | zcat | grep ${CONFIG_NAME}