Concurrency and Race Conditions
Concurrency and Race Conditions

---
Concurrency and Its Management
Concurrency and Its Management
- Sources of concurrency
  - Multiple user-space processes
  - Multiple CPUs
  - Device interrupts
- Management
  - Workqueues
  - Tasklets
  - Timers

---
Concurrency and Its Management
- Some guiding principles
  - Avoid shared resources whenever possible
    - Avoid global variables
  - Apply locking and mutual exclusion principles to protect shared resources

---
Concurrency
Application
Application
User Space
Kernel Space
May raise concurrency
read / write
Device Driver
May raise concurrency
interrupter
Hardware
Device

---
Semaphores and Mutexes
Semaphores and Mutexes
- Atomic operation:
  - sequences of instructions that guarantee atomic accesses and updates of shared single word variables
- Critical section:
  - code that can be executed by only one thread at a time
  - Not all critical sections are the same
    - Some involve accesses from interrupt handlers
    - Some have latency constraints
    - Some might hold critical resources

---
Semaphore
Process B
Process A
P function
B is going to sleep while A is
Critical Section
V function

---
The Linux Semaphore Implementation
The Linux Semaphore Implementation
To declare and initialize a semaphore, call
To initialize a dynamically allocated semaphore, call
#include <asm/semaphore.h>
void sema_init(struct semaphore *sem, int val);
DECLARE_MUTEX(name); /* initialized to 1 */
DECLARE_MUTEX_LOCKED(name); /* initialized to 0 */
void init_MUTEX(struct semaphore *sem);
void init_MUTEX_LOCKED(struct semaphore *sem);

---
The Linux Semaphore Implementation
For the P function, call
- down
  - Just waits for the critical section
    - Until the cows come home
void down(struct semaphore *sem);
void down_interruptible(struct semaphore *sem);
void down_trylock(struct semaphore *sem);

---
Using Semaphores in scull
Sample Using Semaphores

---
Sample Using Semaphores
Critical section

---
Example
sht21.c
static ssize_t eic_show(struct device *dev,
struct device_attribute *attr,
char *buf)
{
struct sht21 *sht21 = dev_get_drvdata(dev);
int ret;
ret = sizeof(sht21->eic) - 1;
mutex_lock(&sht21->lock);
if (!sht21->eic[0])
ret = eic_read(sht21);
if (ret > 0)
memcpy(buf, sht21->eic, ret);
mutex_unlock(&sht21->lock);
return ret;
}

---
Spinlocks
Spinlocks
- Used in code that cannot sleep
  - Better performance than semaphores
- Usually implemented as a single bit
  - If the lock is available, the bit is set and the code continues
  - If the lock is taken, the code enters a tight loop
    - Repeatedly checks the lock until it become available

---
Spinlocks
- Actual implementation varies for different architectures
- Protect a process from other CPUs and interrupts

---
Spinlock
Process A
Process B
P Function
B is going to busy-loop while
A is processing
Critical Section
V Function

---
Introduction to Spinlock API
Introduction to Spinlock API
#include <linux/spinlock.h>
To initialize, declare
spinlock_t my_lock = SPIN_LOCK_UNLOCKED;
void spin_lock_init(spinlock_t *lock);
To acquire a lock, call
void spin_lock(spinlock_t *lock);
To release a lock, call
void spin_unlock(spinlock_t *lock);

---
Spinlocks and Atomic Context
Spinlocks and Atomic Context
- While holding a spinlock, be atomic
  - Do not sleep or relinquish the processor
    - Examples of calls that can sleep
      - Copying data to or from user space
        - User-space page may need to be on disk…
      - Memory allocation
        - Memory might not be available
  - Disable interrupts (on the local CPU) as needed
- Hold spinlocks for the minimum time possible

---
The Spinlock Functions
The Spinlock Functions
The functions to acquire a spinlock
  void spin_lock(spinlock_t *lock);
  /* disables interrupts on the local CPU */
  void spin_lock_irqsave(spinlock_t *lock,
  unsigned long flags);
  /* used as the only process that disables interrupts */
  void spin_lock_irq(spinlock_t *lock);

---
Sample - spinlock

---
Sample - spinlock

---
Example
gpio_keys.c
static void gpio_keys_irq_timer(struct timer_list *t)
{
struct gpio_button_data *bdata = from_timer(bdata, t, release_timer);
struct input_dev *input = bdata->input;
unsigned long flags;
spin_lock_irqsave(&bdata->lock, flags);
if (bdata->key_pressed) {
input_event(input, EV_KEY, *bdata->code, 0);
input_sync(input);
bdata->key_pressed = false;
}
spin_unlock_irqrestore(&bdata->lock, flags);
}

---
Atomic Variables
Atomic Variables
- If the shared resource is an integer value
  - Locking is too expensive
- The kernel provides an atomic integer type, atomic_t
  - Should not count on atomic_t holding > 24 bits
  - atomic_t data must be access through special functions (<asm/atomic.h>)
  - SMP safe

---
Atomic Variables
- Atomic variables might not be sufficient
  - atomic_set(v, i);
  - atomic_read(v);

---
Example
linux-4.20.7/drivers/gpu/drm/exynos/exynos_drm_fimd.c
static void fimd_trigger(struct device *dev)
{
…….
if (atomic_read(&ctx->triggering))
return;
/* Enters triggering mode */
atomic_set(&ctx->triggering, 1);
        …….
/*
* Exits triggering mode if vblank is not enabled yet, because when the
* VIDINTCON0 register is not set, it can not exit from triggering mode.
*/
if (!test_bit(0, &ctx->irq_flags))
   atomic_set(&ctx->triggering, 0);
}