I2C Driver

---
I2C
- Inter-Integrated Circuit
- Simple, low-bandwidth, short-distance protocol
- Speed, Max 400Kbps
- Philips originally developed I2C, current is NXP
- I2C is a two-wire serial bus
  - SDA → Data
  - SCL → Clock
- Controller : host, adapter, master
- Device : device, client, slave
https://web.archive.org/web/20070926222250/http://embedded.com/story/OEG20010718S0073

---
I2C Protocol
- Serial bus
  - SDA data line
  - SCL clock line
https://en.wikipedia.org/wiki/I%C2%B2C

---
I2C Master and Client
RK3399 SOC
SHT21 sensor
SCL
I2C Master
I2C Client
SDA

---
I2C Protocol
Ref_Link

---
Linux and I2C
I2C Char Driver
I2C Device Driver
I2C Kernel API
I2C Protocol
RK3399 I2C Driver
https://i2c.wiki.kernel.org/index.php/File:I2c-layers.png

---
I2C Driver – Type 1
i2c_Tool
User space
/dev/i2c-dev-X
Kernel space
i2c-core.c
I2c-dev.c
I2C drivers
i2c-rk3x.c
Adapter Driver
Hardware
Device

---
I2C Driver – Type 2
Application
User space
/sys/class/hwmon/
Kernel space
I2C stack drivers
hwmon driver
I2c-core.c
I2c-dev.c
hwmon
I2C adapter drivers
i2c-rkxx.c
SHT21 Driver
Hardware
SHT21 Sensor

---
I2C Host Driver

---
I2C Host Driver
- I2C Host driver
  - ${kernel}/drivers/i2c/
    - i2c-core.c
    - i2c-dev.c
    - i2c-smbus.c
    - i2c-rk3x.c
    - i2c-gpio.c
I2C Device Tree
DTS Node
PinMux

---
I2C Master and Client
RK3399 SOC
SHT21 sensor
i2c-rkxx.c
SCL
I2C Master
I2C Client
SDA

---
I2C Adapter Model
linux/i2c.h

---
I2C Driver – i2c-core.c
- I2c-core stack core
- Export I2C kernel API
- Construct I2C subsystem

---
I2C Driver – i2c-rk3x.c
- I2C bus implement in SOC
- Register for i2c-core.c
- Communication with I2C device
Up-Layer
Adapter
i2c-rk3x.c
Driver
Hardware
Device
Register

---
I2C Char Driver – i2c-dev.c
- Register a I2C character driver
- Use I2C kernel API to control I2C device
- Convenient implement user-space driver
User space
/dev/i2c-dev-x
Kernel
Character Core
I2c-dev.c
spi.c
Register

---
I2C Adapter – GPIO Emulator
- I2C Host Driver – GPIO
  - rockchip-rk3399-nanopi-m4/drivers/i2c/busse/i2c-gpio.c
DTS

---
I2C Host – GPIO Emulator
i2c_Tool
User space
/dev/i2c-dev-X
Kernel space
i2c-core.c
I2c-dev.c
I2C drivers
I2c-gpio.c
i2c-algo-bit.c
RK-GPIO
Hardware
I2C Device

---
I2C Client Driver

---
I2C Client Driver
RK3399 SOC
SHT21 sensor
EEPROM
SCL
SCL
I2C Host
I2C Client
SDA

---
I2C Client Driver – EEPROM - 1
Application
User space
/dev/at24cxx
Kernel space
I2C stack drivers
I2c-core.c
I2c-dev.c
Character Driver
I2C adapter drivers
i2c-rk3x.c
At24c08 Sample
Driver
Hardware
EEPROM

---
I2C Client Driver – EEPROM - 2
Application
User space
/sys/class/eeprom/
Kernel space
I2C stack drivers
I2c-core.c
I2c-dev.c
SYSFS API
I2C adapter drivers
i2c-rk3x.c
drivers/misc/at24.c
Hardware
EEPROM

---
AT24C08 I2C Behave
- Byte Write
- Current Address Read

---
AT24C08 I2C Behave
- Random Read
  - Master view

---
I2C Client Driver API
- module_i2c_driver()
- i2c_register_driver(struct module *owner, struct i2c_driver *driver)
- i2c_del_driver(struct i2c_driver *driver)

---
I2C Client Driver – SHT21
3
static int sht21_probe(struct i2c_client *client,
        const struct i2c_device_id *id)
{
}
/* Device ID table */
static const struct i2c_device_id sht21_id[] = {
{ "sht21", 0 },
{ }
};
MODULE_DEVICE_TABLE(i2c, sht21_id);
static struct i2c_driver sht21_driver = {
        .driver.name = "sht21",
        .probe = sht21_probe,
        .id_table = sht21_id,
};
module_i2c_driver(sht21_driver);
Initialize code
For DTS
2
1
rockpi-kernel/drivers/hwmon/sht21.c

---
I2C R/W Kernel API
SMBus Style

---
SMBus
- SMBus is the System Management Bus
  - Define by Intel
  - Personal computers and servers
  - For low-speed system management communications

---
I2C R/W Kernel API - SMBus Style
- Send byte
  - i2c_smbus_write_byte(const struct i2c_client *client, u8 value)
- Receive byte
  - i2c_smbus_read_byte(const struct i2c_client *client)

---
I2C R/W Kernel API - SMBus Style
- Write byte/word
  - i2c_smbus_write_byte_data(const struct i2c_client *client, u8 command, u8 value)

---
I2C R/W Kernel API - SMBus Style
- Read byte/word
  - i2c_smbus_read_byte_data(const struct i2c_client *client, u8 command)

---
I2C R/W Kernel API - SMBus Style
rockpi-kernel/drivers/hwmon/sht21.c
Read
Temperature
Read
Humidity

---
I2C R/W Kernel API
Kernel I2C Style

---
I2C R/W API - Kernel I2C Style
CH5/i2c-subsystem/eeprom_i2c/i2c-at24c08-2
I2C Write
Address offset of Data
Data will be wrote

---
I2C R/W Kernel API - I2C Style
CH5/i2c-subsystem/eeprom_i2c/i2c-at24c08-2
I2C Read
Address offset of Data
Data return

---
I2C Client in User Space

---
Enable I2C-dev
[CMD] make menuconfig

---
I2C Client in User Space IOCTL
- ioctl(file, I2C_SLAVE, long addr)
- ioctl(file, I2C_TENBIT, long select)
- ioctl(file, I2C_FUNCS, unsigned long *funcs)
- ioctl(file, I2C_RDWR, struct i2c_rdwr_ioctl_data *msgset)
- ioctl(file, I2C_SMBUS, struct i2c_smbus_ioctl_data *args)

---
I2C Client in User Space
- ioctl(file, I2C_RDWR, struct i2c_rdwr_ioctl_data *msgset)
- ioctl(file, I2C_SMBUS, struct i2c_smbus_ioctl_data *args)
I2C Style
struct i2c_rdwr_ioctl_data {
struct i2c_msg __user *msgs;	/* pointers to i2c_msgs */
__u32 nmsgs;	/* number of i2c_msgs */
};
struct i2c_smbus_ioctl_data {
__u8 read_write;
__u8 command;
__u32 size;
union i2c_smbus_data __user *data;
};
SMBUS Style

---
I2C Client in User Space - SMBUS Style
3-4-3/eeprom_test_user

---
I2C Client in User Space – SMBUS Style
3-4-3/eeprom_test_user

---
I2C Client in User Space - I2C Style
eeprom_i2c/i2c-kernel-style

---
I2C Client in User Space - I2C Style
eeprom_i2c/i2c-kernel-style