An Introduction to Device Drivers
RK3399 and SOC

---
RockPi WiKi
- Rock Pi Wiki
  - https://wiki.radxa.com/Rockpi4
- Rock Pi Hardware
  - https://wiki.radxa.com/Rockpi4/hardware/rockpi4
- Rock Pi Image
  - https://wiki.radxa.com/Rockpi4/downloads

---
CPU

---
CPU (1)
- Two CPU clusters
  - Big cluster with dual-core Cortex-A72
    - high-performance
  - Little cluster with quad-core Cortex-A53
    - low power

---
CPU (2)
- Arm big.LITTLE technology
  - ”LITTLE” processors are designed for maximum power efficiency
  - ”big” processors are designed to provide maximum compute performance.
LITTLE
big
https://www.arm.com/zh-TW/technologies/big-little

---
Memory

---
Memory
- Internal ROM
  - Internal BootRom (Size : 32KB)
  - boot from
    - SPI, eMMC, SD/MMC
- Internal RAM
  - 200KB
- External
  - DDR3/DDR3L/LPDDR3/LPDDR4
  - SPI NOR/NAND Flash
  - EMMC5.1
  - SD3.0/MMC4.51

---
MMU (1)
32 Bit CPU
Physical Address
Virtual Address

---
MMU (2)
AArch64 Linux memory layout with 4KB pages + 3 levels
64 Bit CPU
512GB
reserved for
kernel-space
512GB
reserved for
user space

---
MMU (3)
- The MMU divides memory into 4KB pages
- 2-level page table structure
  - The First level
    - Page Directory consists of 1024 Directory Table Entries (DTEs)
    - Each pointing to a Page Table.
  - The Second level
    - The Page Table consists of 1024 Page Table Entries (PTEs)
    - Each pointing to a page in memory

---
MMU (4)
31
22
21
12
11
0
DTE index
PTE index
Page Offset

---
MMU (5)
Physical
memory address
I/O Address Mapping
can’t use
physical memory
address direct
Rockchip_RK3399TRM_V1.3_Part1.pdf

---
MMU (6)
DDR SD RAM Memory

---
Interconnect Connect

---
Bus Architecture
- AMBA : Advanced Microcontroller Bus Architecture
  - AXI
  - AHB
  - APB
https://www.arm.com/zh-TW/architecture/system-architectures/amba

---
GPU

---
Graphics Engine (1)
- Graphics Process Unit
- Mali-T860MP4 GPU
  - OpenGL ES1.1/2.0/3.0, OpenCL1.2,
  - 3DGraphics Engine
  - 2D Graphics Engine
Rockchip_RK3399TRM_V1.3_Part1.pdf

---
Graphics Engine (2)
- OpenGL
  - Open Graphics Library
- OpenGL ES
  - OpenGL for Embedded Systems
- EGL
  - Native Platform Graphics Interface
https://www.khronos.org/egl

---
Graphics Engine (3)
https://en.wikipedia.org/wiki/EGL_%28API%29#/media/File:Wayland_display_server_protocol.svg

---
Connect

---
USB (1)
- USB Host
  - RK3399
  - OHCI : 1.1.	Hardware Complex
  - UHCI : 1.0, 1.1	Software Complex
  - EHCI : 2.0
  - XHCI : 3.0
- USB Device
  - USB Storage

---
USB (2)
- USB OTG
  - USB_ID信號爲低時，該設備應作爲Host
  - USB_ID信號爲高時，該設備作爲Slave

---
UART
- The Universal Asynchronous Receiver/Transmitter
  - Write Data
    - CPU → Data → APB → UART
  - Read Data
    - Data → UART → APB → CPU
PC
RockPi4B
TX
TX
RX
RX
GND
GND
Rockchip_RK3399TRM_V1.3_Part2.pdf

---
I2C (1)
- Serial bus
  - SDA data line
  - SCL clock line
Protocol
https://en.wikipedia.org/wiki/I%C2%B2C

---
I2C (2)
Master and Client
RK3399 SOC
SHT21 sensor
SCL
I2C Master
I2C Client
SDA

---
I2C protocol - Write
Write
  - byte write
  - page write
- Device address
- Read/write bit : 0
- ACK

---
I2C protocol - Read
Read
  - byte read
  - page read
- Device address
- Read/write bit : 1
- ACK

---
GPIO
- General Purpose Programming I/O
- GPIO controls the output data and direction of external I/O pads

---
WiFi Basic

---
WIFI – 802.11 (1)
IEEE 802.11 – 無線區域網路
https://ptolemy.berkeley.edu/projects/ofdm/ergen/docs/IEEE-802.11overview.ppt
Application
Presentation
Session
Transport
Network
Data Link
Physical
ISO
OSI
7-layer
model
Logical Link Control
Medium Access (MAC)
Physical (PHY)
IEEE 802
standards

---
WIFI – 802.11 (2)
https://zh.wikipedia.org/wiki/IEEE_802.11a-1999

---
WIFI – Linux & 802.11 (1)
https://hackmd.io/@0xff07/BJkDzazVK#iwd

---
WIFI – Linux & 802.11 (2)
- Mac80211
  - most associated to hardware offloading
  - the 802.11 protocol state machine lives here
- cfg80211
  - middle-layer Handles Everything Configurable
- nl80211
  - The API between user-land and kernel-land
  - Relies on the netlink protocol to exchange messages between the two worlds
https://www.linuxembedded.fr/2020/05/emulating-wlan-in-linux-part-i-the-80211-stack

---
WIFI – Tool
- Show / manipulate wireless devices and their configuration
  - iw
- For connecting to a WPA/WPA2 network
  - wpa_supplicant

---
Audio

---
ALSA Overview
- Advanced Linux Sound Architecture
  - Linux kernel
  - Software framework
- Sound Servers
  - PulseAudio, JACK ...
- ALSA stream is a data flow representing sound
  - PCM (Pulse-code modulation)
https://en.wikipedia.org/wiki/Advanced_Linux_Sound_Architecture

---
ALSA Overview
- Audio Codec
  - Audio Codec就是音樂訊號（Audio）壓縮/解壓縮(Compress/DECompress)
    的演算法或程式, 前後加起來就是Audio Codec.
- Parameters of the hardware
  - sampling rate : 44100 Hz
  - sample width : 8 bit, 16 bit, 24 bit
  - sample encoding : endianness
  - number of channels : 1 channel, 2 channel ...
https://en.wikipedia.org/wiki/Advanced_Linux_Sound_Architecture

---
ALSA Overview
https://www.researchgate.net/figure/Structure-of-ASoC-and-the-embedment-into-the-Linux-audio-framework_fig2_262112720

---
Sound Card in Linux (1)
[CMD] ls /proc/asound/ -l
lrwxrwxrwx	1 root root 5 Apr 30 06:51 HDMICODEC -> card1
dr-xr-xr-x	4 root root 0 Apr 30 06:51 card0
dr-xr-xr-x	3 root root 0 Apr 30 06:51 card1
-r--r--r--	1 root root 0 Apr 30 06:51 cards
-r--r--r--	1 root root 0 Apr 30 06:51 devices
-r--r--r--	1 root root 0 Apr 30 06:51 hwdep
-r--r--r--	1 root root 0 Apr 30 06:51 pcm
lrwxrwxrwx	1 root root 5 Apr 30 06:51 rockchipes8316c -> card0
dr-xr-xr-x	2 root root 0 Apr 30 06:51 seq
-r--r--r--	1 root root 0 Apr 30 06:51 timers
-r--r--r--	1 root root 0 Apr 30 06:51 version

---
Sound Card in Linux (2)
Sound card 0
[CMD] cat /proc/asound/cards
 0 [rockchipes8316c]:	rockchip_es8316 - rockchip,es8316-codec
        rockchip,es8316-codec
 1 [HDMICODEC ]: HDMI-CODEC - HDMI-CODEC
        HDMI-CODEC
Sound card 1

---
Sound Card in Linux (3)
rockchipes8316c
[CMD] ls -l /proc/asound/card0/
-r--r--r-- 1 root root 0 Apr 30 06:59 id
dr-xr-xr-x 3 root root 0 Apr 30 06:59 pcm0c
dr-xr-xr-x 3 root root 0 Apr 30 06:59 pcm0p
capture
playback
[CMD] ls -l /proc/asound/card1/
-r--r--r-- 1 root root 0 Apr 30 07:01 id
dr-xr-xr-x 3 root root 0 Apr 30 07:01 pcm0p

---
Linux Display Subsystem

---
Linux Windows System (1)
https://en.wikipedia.org/wiki/File:X_client_sever_example.svg

---
Linux Windows System (2)
https://upload.wikimedia.org/wikipedia/commons/2/2d/The_Linux_Graphics_Stack_and_glamor.svg

---
Linux Windows System (3)
Wayland is a replacement for the X11 window system protocol
https://wayland.freedesktop.org/architecture.html

---
Wayland Display Server and EGL
https://www.wikiwand.com/ja/Wayland

---
GTK and Gnome
GTK
GTK (formerly GTK+) is a free and open-source cross-platform widget toolkit for creating graphical user interfaces (GUIs).
GNOME
GNOME is the default desktop environment of many major Linux distributions
originally an acronym for GNU Network Object Model Environment
free and open-source desktop environment for Linux and other Unix-like[10] operating systems
https://en.wikipedia.org/wiki/GNOME
https://en.wikipedia.org/wiki/GTK

---
OpenGL and EGL
EGL
EGL Native Platform Graphics Interface is an interface portable layer for graphics resource management.
works between rendering APIs such as OpenGL ES or OpenVG and the underlying native platform window system
OpenGL
OpenGL (Open Graphics Library) is a cross-language, cross-platform application programming interface (API) for rendering 2D and 3D vector graphics
Mesa
Mesa, also called Mesa3D and The Mesa 3D Graphics Library
it is an open source implementation of OpenGL, Vulkan, and other graphics API specifications
https://www.khronos.org/egl/
https://en.wikipedia.org/wiki/Mesa_(computer_graphics)
https://en.wikipedia.org/wiki/OpenGL

---
Direct Rendering Manager (DRM)
Direct Rendering Manager
Management of buffers and free space within that memory.
Solve Frame buffer driver cannot be used GPU and multi-user process.
DRM consists of
libdrm
libdrm provides a user space library for accessing the DRM
KMS : Kernel Mode Setting
Change resolution and depth
DRI : Direct Rendering Infrastructure
Interfaces to access hardware directly
GEM : Graphics Execution Manager
Buffer management
DRM Driver in kernel side
Access hardware

---
Direct Rendering Manager (DRM)
If no use DRM

---
Direct Rendering Manager (DRM)
https://upload.wikimedia.org/wikipedia/commons/2/2d/The_Linux_Graphics_Stack_and_glamor.svg

---
Direct Rendering Manager (DRM)
Use DRM

---
Kernel Mode Setting (KMS)
- KMS device model
  - CRTCs
  - Connectors
  - Encoders
  - Planes
- Kernel Mode Setting
  - screen resolution
  - color depth and
  - refresh rate

---
Kernel Mode Setting (KMS)
https://www.kernel.org/doc/html/v4.15/gpu/drm-kms.html

---
Kernel Mode Setting (KMS)
https://upload.wikimedia.org/wikipedia/commons/2/2d/The_Linux_Graphics_Stack_and_glamor.svg

---
Kernel Mode Setting (KMS)
https://www.kernel.org/doc/html/v4.15/gpu/drm-kms.html

---
Video Frame Buffer
The frame buffer device provides an abstraction for
the graphics hardware.
Application
memory
User Space
MMAP
Kernel Space
memory
FB Driver

---
Kernel Mode Setting (KMS)
Encode
Connecter
CRTC
FrameBuffer
Planes