An Introduction to Device Drivers
Build Linux Modules

---
Introduction
Linux Kernel
- https://www.kernel.org/
- Kernel source code
- Kernel Documentation
- Linux Cross Reference

---
Kernel Modularization

---
Linux Kernel
User App
System Call
C library
User Space
Device driver
Linux kernel
Kernel Space
Hard ware

---
HelloWorld Module

---
Kernel Module - Hello World
#include <linux/init.h>
#include <linux/module.h>
static int __init hello_init(void)
{
printk("Hello world!!\n");
return 0;
}
static void __exit hello_exit(void)
{
printk("Goodbye, Hello world!!\n");
}
module_init(hello_init);
module_exit(hello_exit);
Install
Remove

---
Build Kernel Module

---
Source Code Type
- Out of Kernel tree
  - the code is outside of the kernel source tree, in a different directory
- Inside the kernel tree
  - it’ll integrated into the kernel configuration compilation process

---
Modules Type
- Build-in to kernel Image
  - Install auto when system start up
  - No depend problem
  - Kernel Image size problem
- Build a Module type
  - Install by insmod command
  - Need confirm depend
  - Down size kernel image

---
Out of Kernel Tree

---
Out of Kernel Tree - Makefile
Driver Build Type
1-3-1-hello_world
Kernel source code path

---
Inside of Kernel Tree

---
Menuconfig (1)
- Details on compiling the kernel
  - Documentation/kbuild
- Menuconfig
  - [CMD] make menuconfig
  - Need ncurses libraries
    - If menuconfig has error, install below package
    - sudo apt-get install libncurses5 libncurses5-dev libncursesw5

---
Menuconfig (2)
Enter menuconfig setting

---
Menuconfig (3)
- Save to .config file
  - Hide file, use [CMD] ls -la to check
  - Involve Driver build options

---
Menuconfig (3) - Kconfig
drivers/char/Kconfig
- Kconfig
- Tristate
    - [ * ] Build in kernel
    - [ m ] Build module
    - [ ] Nothing to build
  - Bool
  - Select
  - Depends
  - Help

---
Menuconfig (4) - Makefile
[CMD] vim drivers/char/Makefile
obj-y = module_name.o
obj-m = module_name.o
obj-$(CONFIG_XXXX) = module_name.o
Example :
    drivers/char/hello_world.c
    drivers/char/Makefile
    drivers/char/Kconfig

---
Menuconfig (5) - Makefile
Build in to kernel image
   → obj-y = module_name.o
Build a kernel module
→ obj-m = module_name.o
Enable kernel driver or not
→ obj-$(CONFIG_XXXX) = module_name.o

---
Menuconfig
Kconfig, .config and Makefile (1)
Kconfig
.config
Makefile

---
Menuconfig
Kconfig, .config and Makefile (2)
Driver Build Type
menuconfig
menuconfig
CONFIG_HELLO_WORLD=m
hello_world.ko
CONFIG_HELLO_WORLD
.config
CONFIG_HELLO_WORLD=y
obj-$(CONFIG_HELLO_WORLD) += hello_world.o
Driver Build
in kernel
Makefile

---
Menuconfig
Source Code In Kernel Tree
- .config
  - menuconfig
- rockchip_linux_defconfig
  - KERNEL_SRC/arm64/configs
- KERNEL_SRC/.config
  - [CMD] vim $KERNEL_SRC/arch/arm64/configs/XXX_defconfig
    - CONFIG_XXXX=y
    - CONFIG_XXXX=m
    - #CONFIG_XXXX is not set

---
Supplement - Module Symbol

---
Symbols exported to modules
- Two macros are used in the kernel to export functions and variables:
  - EXPORT_SYMBOL(symbolname)
    - exports a function or variable to all modules
  - EXPORT_SYMBOL_GPL(symbolname)
    - exports a function or variable only to GPL modules

---
Sample - hello_exprot
1-3-2-hello_exprot

---
Sample - hello_exprot
1-3-2-hello_exprot/hello_file2.c

---
Sample - hello_exprot
1-3-2-hello_exprot/hello_file1.c