IOCTL

---
ioctl
- Simple data transfers
  - Change hardware settings
  - Eject the media
  - Embedded commands in the data stream
  - Driver-specific file systems

---
ioctl
Application
User Space
IOCTL CMD
Kernel Space
Char Driver
Physical
Hardware

---
ioctl
test_led_char_driver
User Space
Led Value
Kernel Space
/dev/leds
Physical
LED

---
Ioctl User Level
User-level interface
int ioctl(int fd, unsigned long cmd, …)
Variable number of arguments
Problematic for the system call interface
In this context, it is meant to pass a single optional argument
Just a way to bypass the type checking
Difficult to audit ioctl calls
E.g., 32-bit vs. 64-bit modes

---
Driver LED
User Land
3-4-2/test_led_char_driver

---
Ioctl Kernel Level
Kernel-level interface
int (*ioctl) (struct inode *inode,
        struct file *filp,
        unsigned int cmd,
        unsigned long arg);
 cmd : is passed from the user unchanged
 arg : can be an integer or a pointer

---
Driver LED
File operator
IOCTL Callback

---
Driver LED
3-4-2/ioctl_leds.c

---
ioctl Commands
- Need a numbering scheme to avoid mistakes
  - Check include/asm/ioctl.h
  - Documentation/ioctl-decoding.txt
    - How to decode the bits of an IOCTL code
  - ioctl-number.txt
    - How to implement and register device/driver ioctl calls

---
ioctl Commands
- A command number uses four bitfields
  - Defined in <linux/ioctl.h>
  - < direction, type, number, size>
  - direction: direction of data transfer
    - _IOC_NONE
    - _IOC_READ
    - _IOC_WRITE
    - _IOC_READ | WRITE

---
ioctl Commands
  - type (ioctl device type)
    - 8-bit magic number
    - Associated with the device
  - number
    - 8-bit sequential number
    - Unique within device
  - size: size of user data involved
    - The width is either 13 or 14 bits
Example ipmi_devintf.c

---
ioctl Commands
- Useful macros to encode ioctl command numbers
  - _IO(type, nr)
  - _IOR(type, nr, datatype)
  - _IOW(type, nr, datatype)
  - _IOWR(type, nr, datatype)
size = sizeof(datatype)

---
ioctl Commands
- Useful macros to decode ioctl command numbers
  - _IOC_DIR(nr)
  - _IOC_TYPE(nr)
  - _IOC_NR(nr)
  - _IOC_SIZE(nr)

---
ioctl
I2c-dev.c

---
Driver IOCTL
3-4-1

---
Driver IOCTL

---
Driver IOCTL Test
CMD : Reset Value
CMD : Get Value
CMD : Set Value