Platform Driver

---
Platform Driver
- A Driver model interface to the platform bus
- Used to integrate peripherals on many SOC processors
- The platform devices are the devices that are directly
  connected to the CPU, without any kind of bus.
- Platform devices is not a char device ,block device and
  network device

---
Platform Driver

---
Platform Driver Model
linux/platform_device.h
Other driver
Platform driver
Platform device
Platform bus
pseudo-bus
 driver
device
bus
Kobject/kset/ktype

---
Platform Drivers Model
https://elixir.bootlin.com/linux/latest/source/include/linux/platform_device.h#L209

---
Platform Driver Register
Kernel API
Register a driver for platform-level devices
int platform_driver_register(struct platform_driver *drv);
Unregister an array of platform drivers
void platform_unregister_drivers(struct platform_driver * const *drivers,
        unsigned int count);

---
Platform Driver Register
drivers/i2c/busses/i2c-rk3x.c

---
Driver LED
2-4-1-led-gpio

---
Driver LED
Register a led driver
callback function

---
Platform Driver Probe

---
Platform Driver Probe
- Standard driver model convention
- Provide probe() and remove() methods
- Support power management and shutdown
- notifications using the standard conventions

---
Platform Driver Model
probe() should general verify that the specified
device hardware actually exists
struct platform_driver {
        int (*probe)(struct platform_device *);
       int (*remove)(struct platform_device *);
        void (*shutdown)(struct platform_device *);
        int (*suspend)(struct platform_device *, pm_message_t state);
        int (*resume)(struct platform_device *);
        struct device_driver driver;
        const struct platform_device_id *id_table;
        bool prevent_deferred_probe;
};

---
I2C Host Driver
drivers/i2c/busses/i2c-rk3x.c
static struct platform_driver rk3x_i2c_driver = {
.probe = rk3x_i2c_probe,
.remove = rk3x_i2c_remove,
.driver = {
.name = "rk3x-i2c",
.of_match_table = rk3x_i2c_match,
.pm = &rk3x_i2c_pm_ops,
},
};
module_platform_driver(rk3x_i2c_driver);

---
Driver I2C Host (DTS)
arch/arm64/boot/dts/rockchip/rk3399.dtsi
i2c0: i2c@ff3c0000 {
compatible = "rockchip,rk3399-i2c";
reg = <0x0 0xff3c0000 0x0 0x1000>;
clocks = <&pmucru SCLK_I2C0_PMU>,
        <&pmucru PCLK_I2C0_PMU>;
clock-names = "i2c", "pclk";
interrupts = <GIC_SPI 57 IRQ_TYPE_LEVEL_HIGH 0>;
pinctrl-names = "default";
pinctrl-0 = <&i2c0_xfer>;
#address-cells = <1>;
#size-cells = <0>;
status = "disabled";
};

---
I2C Host Driver
static const struct of_device_id rk3x_i2c_match[] = {
{
.compatible = "rockchip,rv1108-i2c",
.data = (void *)&rv1108_soc_data
},
        ...
{
.compatible = "rockchip,rk3399-i2c",
.data = (void *)&rk3399_soc_data
},
{},
};
MODULE_DEVICE_TABLE(of, rk3x_i2c_match);
DTS Check

---
I2C Host Driver
Driver Entry

---
Platform Device

---
Platform Device
- This includes
  - Host bridges to peripheral buses
  - Most controllers integrated into system-on-chip platforms
- A platform_device will be connected through a software bus

---
Platform Device Model
- Defined at <linux/platform_device.h>
- resources include such as addresses and IRQs

---
Driver I2C
Get IO
Memory
Get IRQ

---
Driver I2C Host (DTS)
arch/arm64/boot/dts/rockchip/rk3399.dtsi
i2c0: i2c@ff3c0000 {
compatible = "rockchip,rk3399-i2c";
reg = <0x0 0xff3c0000 0x0 0x1000>;
clocks = <&pmucru SCLK_I2C0_PMU>,
        <&pmucru PCLK_I2C0_PMU>;
clock-names = "i2c", "pclk";
interrupts = <GIC_SPI 57 IRQ_TYPE_LEVEL_HIGH 0>;
pinctrl-names = "default";
pinctrl-0 = <&i2c0_xfer>;
#address-cells = <1>;
#size-cells = <0>;
status = "disabled";
};
IO Memory
Get IRQ