Communicating with Hardware
IO MEMORY MAP

---
I/O Ports and I/O Memory
I/O Ports and I/O Memory
- Every peripheral device is controlled by writing and reading its registers
  - memory address space (memory-mapped I/O)
    - Can access devices like memory
  - I/O address space (port-mapped I/O)
    - Need to use special instructions

---
I/O Ports and I/O Memory
CPU
IO Reg
OutPort
Memory
Controll
Input Port
Memory
IO Address
I/O Port
I/O Memory

---
Physical and Virtual Memory
32 Bit CPU

---
Virtual Memory Organization
AArch64 Linux memory layout with 4KB pages + 3 levels
64 Bit CPU
512GB
reserved for
kernel-space
512GB
reserved for
user space

---
RK3399 Block Diagram

---
RK3399 Memory Map
Physical
memory address
Rockchip_RK3399TRM_V1.3_Part1.pdf
2.1 Address Mapping
can’t use
physical memory
address direct

---
IO REMAP

---
I/O Memory Allocation and Mapping
To make memory accessible, call
https://elixir.bootlin.com/linux/latest/source/arch/arm/include/asm/io.h#L386

---
Video Capture Driver BT878
Get IO MEM
IO MEM remap

---
I/O Memory Allocation and Mapping
https://elixir.bootlin.com/linux/latest/source/include/linux/device.h#L234

---
Driver I2C Bus
rockpi-kernel/drivers/i2c/busses/i2c-rk3x.c

---
Driver I2C Bus
Get IO Memory Address then remap for system (Form DTS)
struct resource *mem;
mem = platform_get_resource(pdev, IORESOURCE_MEM, 0);
i2c->regs = devm_ioremap_resource(&pdev->dev, mem);

---
Driver I2C Bus

---
Driver I2C Bus
P29 of Rockchip_RK3399TRM_V1.3_Part1.pdf

---
IO Read / Write

---
Driver I2C Bus
arm/include/asm/io.h

---
Driver I2C Bus
i2c-rk3x.c

---
Driver I2C Bus
i2c-rk3x.c

---
Driver I2C Bus
Rockchip_RK3399TRM_V1.3_Part2.pdf

---
Driver I2C Bus
Read I2C control register (RKI2C_CON)
u32 val = i2c_readl(i2c, REG_CON) & REG_CON_TUNING_MASK;